## Slide 2
Data Communications and Networks

## Slide 3
01010101
01010101
Data Communication
Data communications are the exchange of data between two devices via some form of transmission medium such as a wire cable.
Notes: The distance over which data moves within a computer may vary from a few thousandths of an inch, as is the case within a single IC chip, to as much as several feet along the backplane of the main circuit board. Over such small distances, digital data may be transmitted as direct, two-level electrical signals over simple copper conductors. Except for the fastest computers, circuit designers are not very concerned about the shape of the conductor or the analog characteristics of signal transmission. Frequently, however, data must be sent beyond the local circuitry that constitutes a computer. In many cases, the distances involved may be enormous. Unfortunately, as the distance between the source of a message and its destination increases, accurate transmission becomes increasingly difficult. This results from the electrical distortion of signals traveling through long conductors, and from noise added to the signal as it propagates through a transmission medium. Although some precautions must be taken for data exchange within a computer, the biggest problems occur when data is transferred to devices outside the computer's circuitry. In this case, distortion and noise can become so severe that information is lost. Data Communications concerns the transmission of digital messages to devices external to the message source. "External" devices are generally thought of as being independently powered circuitry that exists beyond the chassis of a computer or other digital message source. As a rule, the maximum permissible transmission rate of a message is directly proportional to signal power, and inversely proportional to channel noise. It is the aim of any communications system to provide the highest possible transmission rate at the lowest possible power and with the least possible noise.

## Slide 4
Data Communication Model
Source
Transmitter
Transmission System
Receiver
Destination
Digital bit stream
Digital bit stream
Analog Signal
Analog Signal
Text
Text
Notes: Data Communications is the transfer of data or information between a source and a receiver. The source transmits the data and the receiver receives it. Data communication involved the following like communication networks, different communication services required, the kind of networks available, protocol architectures, OSI models, TCP/IP protocol models etc. Data Communication is interested in the transfer of data, the method of transfer and the preservation of the data during the transfer process. In Local Area Networks, we are interested in "connectivity", connecting computers together to share resources. Even though the computers can have different disk operating systems, languages, cabling and locations, they still can communicate to one another and share resources. The purpose of Data Communications is to provide the rules and regulations that allow computers with different disk operating systems, languages, cabling and locations to share resources. The rules and regulations are called protocols and standards in Data Communications.
Source It is the generator of data that will pass on the destination using networks. Without any request source never passes the data to destination. So, if source is passing the data means any of the destinations is requesting for data using some query languages. Transmitter It is simply a device used to convert the data as per the destination requirement. For example a modem, converts the analog (telephonic signals) signal to digital (computer signals) signals and alternatively digital to analog also. Transmission System To transmit the data on different connected systems we use different transmission systems. Data transmission using transmission system means the physical transfer of data over point-to-point or point-to-multipoint communication channels. Example of such channels are copper wires, optical fibers even wireless communication channels etc. Receiver This receives the signals from the transmission system and converts it into a form that is suitable to the destination device. For example, a modem accepts analog signal from a transmission channel and transforms it into digital bit stream which is acceptable by computer system. Destination It is simply a device for which source device sends the data.

## Slide 5
Open System Interconnection (OSI) includes set of protocols that attempt to define and standardize the data communication process defined by International Standardization for Organizations.
OSI Reference Model
Serves as the window for users and application processes to access the network services
Formats the data to be presented to the application layer. It can be viewed as the “Translator” for network
Allows session establishment between processes running on different stations
Ensure the messages are delivered error-free, in sequence, and with no losses or duplications
Controls the operations of the subnet, deciding which physical path the data takes
Provides error-free transfer of data frames from one node to another over the Physical layer
Concerned with the transmission and reception of the unstructured raw bit stream over the physical medium
Data Link
Network
Transport
Session
Presentation
Application
Physical
Data from any software
Connected via LAN
0101
Same process in reverse
Data

## Slide 6
The 5-layer model serves primarily the protocols known as Transmission Control Protocol (TCP) and Internet Protocol (IP), or jointly, TCP/IP. The 5-layer model was developed along with these protocols, antedating the 7-layer model
TCP/IP Reference Model
Represents data to the user plus encoding and dialog control
Supports Communication between diverse devices across diverse network
Determines the best path through the network
Controls the hardware devices and media that make up the network
TCP and IP, as protocols, deal with software rather than hardware. This layer is generally thought of as referring to all hardware under the Network Layer.
Network Access
Internet
Transport
Application
Physical
Data from any software
Connected via LAN
0101
Same process in reverse
Data

## Slide 7
Protocols & Protocols Architecture
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Transport
Network Access
Internet
HTTP
FTP
SMTP
DNS
RIP
SNMP
SSL
ASCII
Sockets
NetBIOS
TCP
UDP
IPv4(ICMP, IGMP)
IPv6(ND, MLD, ICMPv6)
Ethernet
802.11
Wireless LAN
Frame Relay
ATM

## Slide 8
A local-area network (LAN) is a computer network that spans a relatively small area. Most LANs are confined to a single building or group of building
LAN
Switch

## Slide 9
A computer network that spans a relatively large geographical area. Typically, a WAN consists of two or more local-area networks (LANs).
WAN
Internet

## Slide 10
WAN
Wide area network is used to transfer data over long geographical areas. When the information is carried over longer distances it has to pass more physical and logical environments. In order to develop a WAN one has to use the services of the ISPs. The working of the WAN technologies is limited to the physical layer, data link layer and the network layer of the OSI model.
There are FOUR major WAN Technologies
Circuit Switching
Packet Switching
Frame Relay
ATM

## Slide 11
WAN
Circuit-switched is a type of network in which a physical path is obtained for and dedicated to a single connection between two end-points in the network for the duration of the connection.
Circuit Switching
In Telephone Network
Many Paths are
Possible, only one
path are selected
per call
Telephone
Switch
Telephone
Switch
Telephone
Switch
Telephone
Switch
Telephone
Switch
Once a call established, all communication takes place on this path, or circuit. A circuit is dedicated to this call for the duration of the call

## Slide 12
WAN
Packet-switching relatively small units of data called packets are routed through a network based on the destination address contained within each packet. Breaking communication down into packets allows the same data path to be shared among many users in the network. This type of communication between sender and receiver is known as connectionless
Packet Switching
In Data Network
Many paths may be for a single communication as individual packets routed to a destination
No fixed path established. Packets are routed according t the best path available at the time

## Slide 13
WAN
Frame relay is a fast, connection-oriented, packet-switching technology (based on the older packet switching technology) originally intended for use in Integrated Services Digital Network (ISDN) networks, but now widely used in a variety of local and wide area networks
Frame Relay
In Public Network

## Slide 14
WAN
ATM (asynchronous transfer mode) is a dedicated-connection switching technology that organizes digital data into 53-byte cell units and transmits them over a physical medium using digital signal technology. Individually, a cell is processed asynchronously relative to other related cells and is queued before being multiplexed over the transmission path
ATM
Switch
Server
= 53 – byte cells

## Slide 15
Network Topology
Topology refers to the way in which the network of Computers is connected. Each topology is suited to specific tasks and has its own advantages and disadvantages.
The choice of topology is dependent upon
Type and number of equipment being used
Planned applications and rate of data transfers
Required response times
Cost
There are FOUR major competing topologies
Bus
Tree
Ring
Star

## Slide 16
BUS
A bus topology consists of a main run of cable with a terminator at each end. All nodes (file server, workstations, and peripherals) are connected to the linear cable.
PC2
PC1
PC3
PC4
PC5
Send data to PC3
Received data from PC4
Discard
Discard

## Slide 17
RING
In a ring network layout, all of the computers are connected to one another in a circle. The data passes from one computer to the next one and then all the way around the ring layout until it reaches the destination computer.
Send data to PC4
Received data from PC1
Reached at source station
PC1
PC2
PC4
PC3
Data not for this PC
Data not for this PC

## Slide 18
TREE
Network cabling scheme in which two or more hubs and/or data centers are connected to one another in a succession of levels to provide redundancy. Also called cascaded star topology or tree network
PC1
PC2
PC3
PC1
PC2
PC4
PC3
Hub
Send data
Hub
Hub
Destroy

## Slide 19
STAR
A star topology operates from a central hub which acts as a base and transmits messages throughout the network. This helps reduce the number of failures within the network, as all external 'nodes' on the machine connect only to the central hub or switch.
Switch
PC2
PC1
PC3
PC4
PC5
Hub

## Slide 20
Transmission from transmitter to receiver goes over some transmission medium using electromagnetic waves. The first layer (physical layer) of Communication Networks the OSI Seven layer model is dedicated to the transmission media.
When choosing the transmission media, these factors to be considered
Transmission Rate Distances
Cost and Ease of Installation
Resistance to Environmental Conditions
There are TWO types of transmission media
Guided Media
Unguided Media
Transmission Media
Air
Vacuum
Seawater
Twisted Pair Cable
Coaxial Cable
Fiber-Optical Cable
Guided Media
Unguided Media

## Slide 21
Guided Media
Guided Transmission Media uses a "cabling" system that guides the data signals along a specific path. The data signals are bound by the "cabling" system. Guided Media is also known as Bound Media.
There are THREE guided media commonly used:
Twisted Pair
Coaxial Cable
Optical Fiber

## Slide 22
Twisted Pair
Twisted Pair Cable consists of two copper wires, usually twisted around each other to cancel out any noise in the circuit
Two main type of Twisted Pair Cabling:
Unshielded Twisted Pair (UTP)
Shielded Twisted Pair (STP)

## Slide 23
Unshielded Twisted Pair
UTP is the copper media, inherited from telephony, which is being used for increasingly higher data rates, and is rapidly becoming the de facto standard for horizontal wiring, the connection between, and including, the outlet and the termination in the communication closet.
Protected the copper wire from physical damage
Outer Jacket
Protected the signals from interference
Twisted Pair
Electrically isolates wires from each other and identifies each pair
Color-Coded Plastic Insulation

## Slide 24
Shielded Twisted Pair
STP is type of copper telephone wiring in which each of the two copper wires that are twisted together are coated with an insulating coating that functions as a ground for the wires. The extra covering in shielded twisted pair wiring protects the transmission line from electromagnetic interference leaking into or out of the cable
Protected the copper wire from physical damage
Outer Jacket
Protected the signals from interference
Twisted Pair
Overall Shield
Pair Shields
Electrically isolates wires from each other and identifies each pair
Color-Coded Plastic Insulation

## Slide 25
Coaxial Cable
A type of wire that consists of a center wire surrounded by insulation and then a grounded shield of braided wire. The shield minimizes electrical and radio frequency interference. Coaxial cabling is the primary type of cabling used by the cable television industry and is also widely used for computer networks, such as Ethernet.
Plastic Jacket
Metallic Shield
Dielectric Insulator
Center Core

## Slide 26
Optical Fiber
Fiber-optic communication is a method of transmitting information from one place to another by sending pulses of light through an optical fiber. The light forms an electromagnetic carrier wave that is modulated to carry information
Optical fiber transmits a signal-encoded beam of light by means of total internal reflection. Total internal reflection can occur in any transparent medium that has a higher index of refraction than the surrounding medium. In effect, the optical fiber acts as a waveguide for frequencies in the range of about to Hertz; this covers portions of the infrared and visible spectra.

## Slide 27
Optical Fiber Transmission Modes
Graded-index fiber
125µm
50-100
µm
Simple mode fiber
125µm
-10µm
Step-index fiber
Output
pulse
380µm
200µm
Index of
refraction
Input
pulse

## Slide 28
Optical Fiber
Black polyurethane outer jacket
Buffer jacket
Strength member
Silicone coating
Core (silica)
Fiber-optic cable itself is composed of a core glass fiber surrounded by cladding.
Cladding (silica)

## Slide 29
Unguided Media
Unguided transmission media are methods that allow the transmission of data without the use of physical means to define the path it takes. Unguided media provide a means for transmitting electromagnetic waves but do not guide them;
Unguided media, also called wireless communication, transport electromagnetic waves without using a physical conductor; examples unguided media propagation through:
Air
Vacuum
Seawater

## Slide 30
Communication Types
Network switches can operate in either simplex or duplex mode. The distinction makes a fundamental difference in the throughput and reliability of these devices on your network.
There are TWO communication types:
Simplex
Duplex
  Half duplex
  Full duplex

## Slide 31
Simplex
Simplex communication is permanent unidirectional communication. Some of the very first serial connections between computers were simplex connections. Simplex links are built so that the transmitter (the one talking) sends a signal and it's up to the receiving device (the listener) to figure out what was sent and to correctly do what it was told. No traffic is possible in the other direction across the same connection.
Direction of data
Simplex Transmission Mode

## Slide 32
Switch
Switch

## Slide 34
Optical Fiber
High-density polyurethane Jacket
.9” diameter
Metal armor
Rip cord
Inner sheath
Water-blocking tape
Core tube
Each of 12 ribbons has 24 fibers
Dielectric strength number

## Slide 35
Fiber-optic communication is a method of transmitting information from one place to another by sending pulses of light through an optical fiber. The light forms an electromagnetic carrier wave that is modulated to carry information
Optical fiber transmits a signal-encoded beam of light by means of total internal reflection. Total internal reflection can occur in any transparent medium that has a higher index of refraction than the surrounding medium. In effect, the optical fiber acts as a waveguide for frequencies in the range of about to Hertz; this covers portions of the infrared and visible spectra.
Optical Fiber
Transmission Modes
(a) Step-index multimode
(b) Graded-index multimode
(c) Simple mode
Light from a source enters the cylindrical glass or plastic core. Rays at shallow angles are reflected and propagated along the fiber; other rays are absorbed by the surrounding material. This form of propagation is called step-index multimode, referring to the variety of angles that will reflect.
Put another way, the need to leave spacing between the pulses limits data rate. This type of fiber is best suited for transmission over very short distances. When the fiber core radius is reduced, fewer angles will reflect. By reducing the radius of the core to the order of a wavelength, only a single angle or mode can pass: the axial ray.
Graded-index multimode is intermediate between the other two in characteristics. The higher refractive index at the center makes the light rays moving down the axis advance more slowly than those near the cladding. Rather than zig-zagging off the cladding, light in the core curves helically because of the graded index, reducing its travel distance. The shortened path and higher speed allows light at the periphery to arrive at a receiver at about the same time as the straight rays in the core axis.

## Slide 36
Open System Interconnection (OSI) includes set of protocols that attempt to define and standardize the data communication process defined by International Standardization for Organizations.
OSI Reference Model
Application
Presentation
Session
Transport
Network
Data Link
Serves as the window for users and application processes to access the network services
Formats the data to be presented to the application layer. It can be viewed as the “Translator” for network
Allows session establishment between processes running on different stations
Ensure the messages are delivered error-free, in sequence, and with no losses or duplications
Controls the operations of the subnet, deciding which physical path the data takes
Provides error-free transfer of data frames from one node to another over the Physical layer
Concerned with the transmission and reception of the unstructured raw bit stream over the physical medium
010101
Physical

## Slide 37
The 5-layer model serves primarily the protocols known as Transmission Control Protocol (TCP) and Internet Protocol (IP), or jointly, TCP/IP. The 5-layer model was developed along with these protocols, antedating the 7-layer model
Represents data to the user plus encoding and dialog control
Supports Communication between diverse devices across diverse network
Determines the best path through the network
Controls the hardware devices and media that make up the network
Not really part of the model, since TCP and IP, as protocols, deal with software rather than hardware. This layer is generally thought of as referring to all hardware under the Network Layer.
TCP/IP Reference Model
Application
Transport
Network Access
Physical
Internet