## Slide 1
Data Communication & Networking
Data Communication is exchange of data between two devices , via any transmission media

## Slide 2
Communication Model
Communication System Shows the Exchange of Data between two parties.
Output Information
(Exact copy of Original Message)
Destination
Output Data
(sequence of bits)
Receiver
Received Signal
Transmission System
Transmitted Signal
Transmitter
Input data
(Sequence of voltage shifts)
Source
Input
Information
(Message)
Source System
Destination System

## Slide 3
TRANSMISSION MEDIA
Mode of communication, through which signal is carried from one system to another
Two Major Classes
  Guided Media
  Unguided media

## Slide 4
Guided Media
Guided Transmission media uses a cabling system that guides the data signals along a specific path. The data signals are bound by the “Cabling” system.
RJ-45 Connector
Coaxial Cable
Outer Jacket
Braided shield
Foil Shield
Center Conductor
Dielectric
Outer Jacket
Twisted Pair
Color coded plastic insulation
UTP cat5 Cable

## Slide 5
Un-guided media
The unguided media is the wireless media. It transports electromagnetic waves without using any physical conductor. Signals are normally broadcast through the air and thus are available to any one who has the device capable of receiving them.
Space and satellite communications, Microwave system
Radio Astronomy, Radar Landing system.
Cellular Phones, navigational aids, global positioning system.
Wireless networking system.

## Slide 6
OSI
Reference Model
The OSI model is a set of guidelines that describes the process that should take place when two computers communicate on a network.

## Slide 7
The OSI Model Stack
Physical Layer
Physical layer defines the
relationship between a device and
a transmission medium
Data Link Layer
The open system interconnection (OSI) model divides the complex task of internetworking, into a series of stages known as layers.
Upper layers
Lower layers
Network Layer
Transport Layer
Session layer
Presentation layer
Application layer
Data Link layer provides error
Free transfer of data frames
From one PC to another
over a Physical layer
The network layer breaks large
datagrams into smaller packets
The
Internetwork Protocol identifies each host
with a 32-bit IP address
It keeps track of the packet’s order &
the packets that must be re-sent.
Two transport protocols, TCP and UDP,
sits at the transport layer
transport layer to create and control
conversations (or sessions) between
two computers
The Presentation Layer is where the
human readable programming languages are
translated into machine code instructions
This is the level that the user often interacts with

## Slide 8
Working OSI model
As data is being sent from one computer, it will pass from the top layer to the bottom. On the receiving , the data will then be rebuilt from the bottom layer to the top.
Transport Layer
Physical Layer
Network Layer
Data Link Layer
Session layer
Presentation layer
Application layer
Transport Layer
Physical Layer
Network Layer
Data Link Layer
Session layer
Presentation layer
Application layer

## Slide 9
OSI protocol suite is currently not applied to any Computer Network Protocol, but it is used to create protocol suites like TCP/IP
Although this suite is not applied to any computer network but still some network administrators uses this model as a guidance for troubleshooting, whenever the network is down.
Application of OSI model
Physical Layer
If network cable is plugged in?
Data Link Layer
Do you have a link light?
Network Layer
Are you getting an IP?
Can you ping default gateway?
Session layer
Do you have DNS server information?
Presentation layer
What format is the graphic in? Do you have a viewer for that format?
Application layer
Can your web browser open up another website?
Transport layer
Can you ping 4.2.2.2 but not google.com?

## Slide 10
TCP / IP
Reference Model

## Slide 11
TCP / IP Layers
Physical Layer
Network Access Layer
TCP/IP stands for Transmission Control Protocol/Internet Protocol . It is a set of rules / protocols that transfer the data between computers.
The purpose of TCP is to verify whether the data is transferred from a client to the sever.
The purpose of IP is to move packets of data from mode to mode.
...
Internet Layer
Transport Layer
Application
Layer
Physical Layer covers the physical interface between a data transmission device and a transmission medium or network.
Network Access layer defines details of how data is physically sent through the network. and how they interact with physical medium
Internet layer Internet layer pack data into data packets known as IP datagrams
Transport Layer provides data exchange reliability i.e. data arrive at the destination application and data arrive in the same order in which they were sent.
The TCP and UDP are most commonly used protocols in this layer.
Application layer defines host programs interface with transport layer services to use the network.

## Slide 12
Working Of TCP / IP Layers
Application
Layer
Transport Layer
Physical Layer
Internet Layer
Network Access Layer
As data is being sent from one computer, it will pass from the top layer to the bottom. On the receiving end, the data will then be rebuilt from the bottom layer to the top.
Each layer a packet of information travels through adds what is called a header. each layer a sending packet passes through gains another header . When the packet is being rebuilt on the receiving end, each header is unpackaged the same way

## Slide 13
Hardware
Ethernet
802.11
Wireless LAN
Frame Relay
ATM
Physical Layer
Data Link Layer
Network Layer
Physical Layer
Transport Layer
Session layer
Presentation layer
Application layer
IPv4
IGMP
ICMP
ARP
IPv6
ND
MLD
ICMPv6
Comparison of osi & tcp/ip protocol architecture
TCP
UDP
Sockets
NetBIOS
ASCII
SSL
HTTP
FTP
SMTP
DNS
RIP
SNMP
Network Access Layer
...
Internet Layer
Transport Layer
Application
Layer
?

## Slide 14
Network Types
There are many types of networks which are used world wide these days, both in houses and commercially. These networks are used on the bases of their scale and scope, historical reasons, preferences for networking industries, and their design and implementation issues. LAN and WAN are mostly known and used widely.

## Slide 15
LAN- Local Area Network
A local area network (LAN) is a computer network that interconnects computers in a limited area such as a home, school, computer laboratory, or office building using network media.
2 Types

## Slide 16
1- HAN – Home Area Network
Home area network (HAN) is a residential local area network (LAN) for communication between digital devices typically deployed in the home, usually a small number of personal computers and accessories, such as printers and mobile computing devices. An important function is the sharing of Internet access
Internet
Office
Study
Laptop

## Slide 17
2- SAN - Storage Area Network
SAM technology is used for data storage and it has no use for most of the organization but data oriented organizations. Storage area network connects servers to data storage devices by using Fiber channel technology.
Disk Array
RAID
[ redundant array of independent disks]
JBOD
Server

## Slide 18
PAN – Personal Area Network
Personal area network (PAN) is a computer network designed for communication between computer devices (including telephones and personal digital assistants close to one person).
Internet

## Slide 19
CAN - Campus Area Network
Networking spanning with multiple LANs but smaller than a Metropolitan area network, MAN. This kind of network mostly used in relatively large universities or local business offices and buildings.

## Slide 20
A LAN based on Wi-Fi wireless network technology
WLAN

## Slide 21
MAN - Metropolitan Area Network
This kind of network is not mostly used but it has its own importance for some government bodies and organizations on larger scale. MAN, metropolitan area network falls in middle of LAN and WAN, It covers large span of physical area than LAN but smaller than WAN, such as a city.
City

## Slide 22
WAN is a geographically-dispersed collection of LANs. A network device called a router connects LANs to a WAN. In IP networking, the router maintains both a LAN address and a WAN address.
A WAN differs from a LAN in several important ways. Most WANs (like the Internet) are not owned by any one organization but rather exist under collective or distributed ownership and management. WANs tend to use technology like ATM, Frame Relay and X.25 for connectivity over the longer distances.
WAN - Wide Area Network
?

## Slide 23
Circuit Switching
The most common example of circuit-switching is telephone network
In Circuit-switching, a dedicated communication path is established between two stations through the nodes of network
Circuit switching are ideal for communications that require data to be transmitted in real-time.
Exchange
Exchange
Exchange
Exchange
Disadvantage Of Circuit Switching
Circuit establishment data transfer Circuit disconnect
Network Technologies

## Slide 24
Packet Switching
Internet
3
2
1
In packet-switching data is sent out in a sequence of small chunks, called packets.
Packet-switching networks are more efficient if some amount of delay is acceptable
Priorities can be used. If a node has a number of packets for transmission.
3
2
1
Upper bound on packet length is 1000 bytes
Can perform Data-rate conversion. So two Pcs on different data-rates can exchange data

## Slide 25
1-Data Gram
2- Virtual Circuit
Packet Switching techniques
Each Packet is treated independently without any reference of order. So they may not follow the same route or may arrive out of sequence
The destination will do re-ordering of packets and recover lost packets
A preplanned route is set before any packet is sent
All packets follow the same route so they arrive at same order
3
2
1
3
2
1

## Slide 26
X-25
Uses the virtual circuit approach
A set of international protocols approved
The redundant error checking is done at each node
3
2
1

## Slide 27
Frame relay
Frame Relay is based on the old X.25 packet-switching technology
Frame Relay puts data in a variable-size unit called a frame
Link-to-link reliability is not provided – if a frame is corrupted, it is silently discarded
Frame relay was developed to take advantage of high data rates and low error rates of packet-switching.
Unlike X.25 frame relay is a fast packet technology, which means that the protocol does not attempt to correct errors
F1
F2
4
3
2
1
Frame 1
Frame 2
Frame 3

## Slide 28
atm
Improves on performance of Frame Relay
Based upon 53-byte cells of fixed size
Compatible with twisted-pair, coax, and fiber
C1
C2
A Cell of fixed size of 53 byte

## Slide 29
TOPOLOGIES
In computer networking, topology refers to the layout of connected device

## Slide 30
Topologies types
Network topologies are categorized into the following basic types:
Bus
Ring
Star
Tree
Mesh

## Slide 31
BUS -Topology
Data for PC-4
Data Received
A single cable, is established as a shared communication medium on which devices are attached
  Terminators are attached on both ends
A device wanting to communicate with another device on the network sends a broadcast message onto the wire that all other devices see, but only the intended recipient actually accepts and processes the message.
  Suitable for broadcasting.
  CSMA/CD (carrier sense multiple access/collision detection) And CSMA/CA (carrier sense multiple access/collision avoidance), techniques are used to avoid collision of data.

## Slide 32
Star -Topology
HUB
A star network features a central connection point called a hub node OR Switch ..
  If it is a Hub, the Msg will be broadcasted to every system
  If it is a Switch the Msg will be allocated a buffer memory in which destination address would be stored and msg would be forwarded to the destination only
Compared to the bus topology, a star network generally requires more cable, but a failure in any star network cable will only take down one computer's network access and not the entire LAN
Msg to pc 4
2
4
3
1
Switch

## Slide 33
Tree -Topology
5
4
3
2
1
6
7
Data 1 to 5
Multiple Bus topologies together
Same working as Bus topology
  Supports future expandability
  Attenuation.

## Slide 34
Ring -Topology
Sender is terminator
1
2
3
4
Msg for PC-4
All messages travel through a ring in the same direction (either "clockwise" or "counterclockwise").
Attenuation is solved as each Pc is a repeater

## Slide 35
Ring -Topology
All messages travel through a ring in the same direction (either "clockwise" or "counterclockwise").
Attenuation is solved as each Pc is a repeater
  Logically Ring, but physically Star
  A failure in any cable or device breaks the loop and can take down the entire network.
Msg to pc 2
MSAU
Rin Rout
Rin Rout
Rin Rout
Rin Rout
1
2
3

## Slide 36
Mash -Topology
Mesh topologies involve the concept of routes.
Unlike each of the previous topologies, messages sent on a mesh network can take any of several possible paths from source to destination.
partial mesh networks also exist in which some devices connect only indirectly to others.
A mesh network in which every device connects to every other is called a full mesh. As shown in diagram. In Full mesh each device has n-1 connections.
Partial Mash
Full Mash
?